## Slide 1: Main Challenges for the Compilation of Urban Emission Inventories in Spain, What We Expect of FAIRMODE
José M. Baldasano1,2, Marc Guevara1
1Barcelona Supercomputing Center-Centro Nacional de Supercomputación (BSC-CNS)
2Environmental Modeling Laboratory, Technical University of Catalonia (UPC)
Barcelona, Spain.
FAIRMODE Meeting
April 10-12, 2013 Antwerp, Belgium

## Slide 2: Hermesv2.0 urban emission data for SPAIN: THE case of barcelona

## Slide 3: HERMESv2.0 emission model (AE submitted)
The High-Elective Resolution Modeling Emissions System 2.0 (HERMESv2.0) estimates anthropogenic and biogenic emissions with high spatial (up to 1 km2) and a temporal (1 h) resolution, taking 2009 as the reference period. It represents the core emission of the Spanish air quality forecast system CALIOPE
HERMESv2.0
HERMES-BOUP
Emission inventory specifically developed for Spain, using mainly bottom-up approaches & local info
HERMES-DIS
Spatial/temporal disaggregation and speciation of the original annual gridded CEIP-EMEP emissions
Hourly speciated emissions

## Slide 4: Conceptual framework
HERMES-DIS
HERMES-BOUP
EMEP emission database
Source SNAP sector specific spatial and temporal proxies
MEGAN v 2.04
Biogenic emissions
SNAP01/03/04/09
Local point source inventory with specific data by stack
SNAP05/06/10
INESP emission database
Elemental SNAP activity specific spatial and temporal proxies
Desaggregation Methodology
Bottom-Up approach
Top-Down approach
Down-scaling
SNAP07
Road Network with daily average traffic, speed circulation, vehicle park composition and temporal profiles per stretch
SNAP02
Statistics on fuel consume
Population map
SNAP08
Monthly traffic by airport
Annual ship operations by port
Agricultural vehicle fleet at NUTS 3 level
GIS pre-processing data & Calculation process
Chemical speciation (CBIV, CB05, MELCHIOR2)
Hourly-gridded NOx, NMVOCs, CO, SO2, NH3, TSP, PM10, PM2.5 emissions
Emissions file management
Emission information/visualization
NetCDF, .csv, .kmz,…
Emission data for air quality modeling
CALIOPE (http://www.bsc.es/caliope)

## Slide 5: EMEP-DIS
SNAP | TYPE OF SOURCE | SPATIAL SURROGATES | SOURCES | TEMPORAL SURROGATES
01 | Point | E-PRTR facilities related to SNAP01 (*) Industrial land use (Code 121) | E-PRTR v 3.2 CLC 2000/2006 v15 (**) | MONTHLY and WEEKLY profiles by country and SNAP sector (reported by IER as part of the GENEMIS project) HOURLY profiles by SNAP sector (reported by TNO-MEP for TROTREP/POET)
02 | Area | Urban/industrial land uses (Codes 111, 112, 121, 123 & 124) | CLC 2000/2006 v15 (**) | 
03 | Point | E-PRTR facilities related to SNAP03 (*) Industrial land use (Code 121) | E-PRTR v 3.2 CLC 2006 v15 (**) | 
04 | Point | E-PRTR facilities related to SNAP04 (*) Industrial land use (Code 121) | E-PRTR v 3.2 CLC 2000/2006 v15 (**) | 
05 | Point | E-PRTR facilities related to SNAP05 (*) Ports & Airports Service Stations Industrial land use (Code 121) | E-PRTR v 3.2 GISCO data Tele Atlas ® Multinet ® 2011 CLC 2000/2006 v15 (**) | 
06 | Area | Urban/industrial/construction land uses (Codes 111, 112, 121 & 133) | CLC 2000/2006 v15 (**) | 
07 | Line | Stretch roads discriminated by type of road (6 types from motorways to local roads). Weight factors assigned to each type of road | Tele Atlas ® Multinet ® 2011 | 
08 | Area | Port/Airport land uses (Codes 123 & 124) Industrial/agricultural land uses (Codes 121, 122, 241,242 & 243) | CLC 2000/2006 v15 (**) | 
 | Area | Reallocation of EMEP SHIP emissions considering the maritime routes given by the combination of AMVER and ICOADS data sets | Wang, et al. (2008) | 
09 | Point | E-PRTR facilities related to SNAP09 (*) Industrial/Dump land uses (Codes 121 & 132) | E-PRTR v 3.2 CLC 2006 v15 (**) | 
10 | Area | Agricultural land uses (Codes from 211 to 243 ) | CLC 2000/2006 v15 (**) | 
(*) A relationship between NACE and SNAP activity codes has been carried out (**) CLC 2000 v 15 has been used in Greece due to the lack of data in the CLC 2006 v15 |  |  |  | 

## Slide 6: Principal working domains
D1
D2
D3
D4
D6
D5
Domain | Resolution | Emissions
D1 - Europe | 12km | HERMES-DIS (All)
D2 - IP + Balearic Islands | 4km | HERMES-BOUP (Spain) / HERMES-DIS (Rest of countries + Ship)
D3 – Canary Islands | 2km | HERMES-BOUP (All)
D4 - Andalucia | 1km | HERMES-BOUP (Spain) / HERMES-DIS (Rest of countries + Ship)
D5 – Barcelona Greater Area | 1km | HERMES-BOUP (All except ship emissions)
D6 – Madrid Greater Area | 1km | HERMES-BOUP (All)
D2
D4
D5
D6
Barcelona urban city
Madrid urban city

## Slide 7: Barcelona: Main Characteristics
Population (> 1,500,000 inhabitants)
Energy industries
Manufacturing Industries
Waste Incinerator
Port  (> 8,000 operations/year)
Airport  (> 135,000 LTO/year)
Mean traffic flow > 20,000 veh./day)
Need of specific high resolution local data

## Slide 8: Energy-Industry-Waste (SNAP01/03/04/09)
Facility name
SNAP elemental activity code
Geographical location
Stack height
Activity Factor (annual production or fuel consumption)
Emission Factors for each pollutant
Temporal profiles
Speciation profiles
Local point source inventory
A total of 1,795 point sources considered
Energy
  Emissions are obtained for each power station from measured data reported by CIEMAT (personal communication)
Chart: Energy production (2009-2010-2011)
| Prod. 09 | Prod. 10 | Prod. 11
Coal-Fuel power plant | 45712 | 33630 | 52366
Combined cycled power plant | 82241 | 67961 | 55194
Energy
  Energy mix varies from year to year, which directly affects the emissions
Energy forecasting (demand) would allow to develop a more realistic air quality forecast system
Industry
  Emissions are obtained from measured data reported by XEAC (personal communication) or EMEP/CORINAR/EEA guidebooks
  In some cases, production data is only available for the whole industrial. An assignation among each facility is performed using distributional factors
Lack of specific emission/production data from some large point sources
Waste
  Emissions are obtained from measured data reported by XEAC (personal communication)

## Slide 9: Residential-Commercial (SNAP02)
ACTIVITY DATA
EMISSION FACTORS
SPATIAL & TEMPORAL DISAGGREG.
EEA / EMEP / CORINAIR guidebooks
Population map from Tele Atlas ® Multinet ® 2011 cartography information
Industrial/urban land uses from CORINE Land Cover 2006 v 15 (100m res)
Annual statistics on fuel consumptions (natural gas, gasoil C, GLP, fuel oil, coal and biomass) at NUTS level 3
Monthly/weekly/hourly profiles by type of fuel obtained from national statistics
CLC 2006 v15 (100m)
Population map
Emissions from biomass combustion are allocated in cells with a limit value of population (depending on the domain’s resolution)
Difficulty to find local information and spatial allocation for biomass combustion.
Temporal allocation based on national consumption statistics, but not on specific weather conditions

## Slide 10: Transport – On-road traffic (SNAP07)
Used > 1,000 temporal profiles (including monthly, weekly, hourly)
A complete digital road map with traffic flow information
2,575 Traffic Stations +
870 street km TeleAtlas Multinet
Chart: Hourly profiles - Weekday
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | 0.070193 | 0.015259 | 0.027467 | 0 | 0 | 0.024415 | 0.14954 | 0.84232 | 0.90031 | 1.3245 | 1.7548 | 1.8128 | 1.9959 | 1.9502 | 1.5748 | 1.6724 | 1.9807 | 1.9502 | 2.0631 | 1.648 | 0.94914 | 0.65921 | 0.39369 | 0.2411
 | 0.075015 | 0.033671 | 0.017901 | 0.01236 | 0.03154 | 0.048589 | 0.33842 | 1.4082 | 1.4653 | 1.5097 | 1.6222 | 1.6708 | 1.6908 | 1.6904 | 1.6218 | 1.7415 | 1.6132 | 1.5519 | 1.6699 | 1.551 | 1.1708 | 0.7088 | 0.49015 | 0.26596
 | 0.022553 | 0.011276 | 0.011276 | 0.014352 | 0.070733 | 0.39006 | 1.3675 | 1.4059 | 1.45 | 1.6361 | 1.674 | 1.7073 | 1.7832 | 1.6443 | 1.5925 | 1.5823 | 1.7007 | 1.7863 | 1.6028 | 1.1261 | 0.72681 | 0.44951 | 0.24449 | 0
 | 0.081719 | 0.064208 | 0.019457 | 0.036968 | 0.040859 | 0.12063 | 0.44167 | 0.99035 | 1.2433 | 1.5118 | 1.9146 | 1.9009 | 1.8698 | 1.7998 | 1.7336 | 1.5332 | 1.6772 | 1.8698 | 1.8212 | 1.3912 | 0.82302 | 0.61873 | 0.3152 | 0.18095
 | 0.10877 | 0.023895 | 0.014832 | 0.0074158 | 0.021423 | 0.069214 | 0.29993 | 1.3142 | 1.208 | 1.3719 | 1.6274 | 1.615 | 1.7205 | 1.7477 | 1.7114 | 1.6826 | 1.6133 | 1.8185 | 1.7856 | 1.568 | 1.0811 | 0.78443 | 0.51663 | 0.28839
 | 0.049071 | 0.031227 | 0.0089219 | 0.0089219 | 0.024535 | 0.13383 | 0.8119 | 1.7086 | 1.3985 | 1.4364 | 1.4208 | 1.432 | 1.5747 | 1.6684 | 1.6216 | 1.6327 | 1.6238 | 1.7866 | 1.7732 | 1.5881 | 1.1152 | 0.68699 | 0.34126 | 0.12268
 | 0.025514 | 0.012757 | 0.0042523 | 0.0042523 | 0 | 0 | 0.13607 | 0.81644 | 1.0886 | 1.4118 | 2.3473 | 2.3983 | 2.7215 | 2.1134 | 1.8795 | 1.9603 | 1.7179 | 1.7179 | 1.4075 | 0.96527 | 0.57831 | 0.36145 | 0.20411 | 0.12757
 | 0.14043 | 0.013813 | 0.016115 | 0.0023022 | 0.03223 | 0.073669 | 0.77353 | 1.5424 | 1.234 | 1.2616 | 1.5632 | 1.8164 | 1.6599 | 1.6898 | 1.7312 | 1.8463 | 1.9822 | 1.6622 | 1.6829 | 1.2708 | 0.89784 | 0.54561 | 0.33151 | 0.23022
 | 0.30923 | 0.14038 | 0.071662 | 0.060864 | 0.073626 | 0.1875 | 0.80596 | 1.8986 | 1.6315 | 1.392 | 1.2251 | 1.2575 | 1.2811 | 1.2507 | 1.447 | 1.5236 | 1.2212 | 1.3675 | 1.5697 | 1.5334 | 1.3449 | 1.1437 | 0.80007 | 0.46335
 | 0.19354 | 0.071128 | 0.044662 | 0.043008 | 0.076091 | 0.18526 | 1.0041 | 2.0296 | 1.7914 | 1.4987 | 1.0818 | 1.0884 | 1.0702 | 1.1513 | 1.325 | 1.3432 | 1.3018 | 1.4887 | 1.7749 | 1.8229 | 1.5218 | 1.1017 | 0.64346 | 0.34737
 | 0.17665 | 0.078905 | 0.041219 | 0.038864 | 0.049463 | 0.21434 | 1.0022 | 1.836 | 1.5899 | 1.2519 | 1.1753 | 1.2271 | 1.2566 | 1.4756 | 1.8101 | 1.6134 | 1.2366 | 1.4627 | 1.8125 | 1.5569 | 1.2401 | 0.87384 | 0.59355 | 0.38628
 | 0.12996 | 0.059654 | 0.027696 | 0.038349 | 0.053262 | 0.19387 | 0.9779 | 2.4394 | 2.1923 | 1.4019 | 1.0887 | 1.0929 | 1.1654 | 1.1909 | 1.5041 | 1.5063 | 1.2932 | 1.5915 | 1.813 | 1.4913 | 1.1228 | 0.77976 | 0.53262 | 0.31318
Chart: Hourly profiles - Holiday
 | 0.59 | 0.34 | 0.22 | 0.21 | 0.16 | 0.22 | 0.34 | 0.58 | 0.76 | 0.95 | 1.3 | 1.71 | 2.13 | 2.03 | 1.69 | 0.96 | 0.83 | 1.03 | 1.29 | 1.5 | 1.48 | 1.49 | 1.27 | 0.92
 | 0.45 | 0.22 | 0.16 | 0.14 | 0.12 | 0.15 | 0.28 | 0.45 | 0.72 | 1.07 | 1.44 | 1.6 | 1.97 | 2.14 | 1.75 | 0.99 | 0.96 | 1.46 | 1.5 | 1.6 | 1.68 | 1.37 | 1.09 | 0.7
 | 0.5 | 0.25 | 0.22 | 0.13 | 0.09 | 0.23 | 0.46 | 0.61 | 0.49 | 0.75 | 0.93 | 1.31 | 1.6 | 1.98 | 1.68 | 0.97 | 1.05 | 1.29 | 1.54 | 1.89 | 1.95 | 1.96 | 1.39 | 0.74
 | 0.41 | 0.22 | 0.2 | 0.13 | 0.11 | 0.2 | 0.47 | 0.65 | 0.66 | 1.09 | 1.33 | 1.53 | 1.93 | 1.91 | 1.77 | 1.04 | 1.02 | 1.25 | 1.59 | 1.47 | 1.55 | 1.65 | 1.17 | 0.64
 | 0.42 | 0.32 | 0.14 | 0.13 | 0.19 | 0.27 | 0.51 | 0.55 | 0.54 | 0.75 | 1.28 | 1.5 | 2.01 | 1.88 | 1.56 | 1.24 | 1.17 | 1.34 | 1.67 | 1.63 | 1.62 | 1.36 | 1.15 | 0.76
 | 0.3 | 0.2 | 0.21 | 0.17 | 0.15 | 0.22 | 0.43 | 0.85 | 0.89 | 1.09 | 1.43 | 1.47 | 1.7 | 1.96 | 1.74 | 1.17 | 1.17 | 1.32 | 1.44 | 1.77 | 1.64 | 1.26 | 0.87 | 0.56
 | 0.56 | 0.4 | 0.26 | 0.22 | 0.17 | 0.31 | 0.57 | 0.7 | 0.88 | 1.05 | 1.32 | 1.54 | 1.61 | 1.75 | 1.68 | 1.01 | 0.97 | 1.23 | 1.43 | 1.5 | 1.49 | 1.3 | 1.09 | 0.94
 | 0.32 | 0.18 | 0.14 | 0.13 | 0.16 | 0.23 | 0.55 | 0.71 | 0.86 | 1.11 | 1.43 | 1.84 | 1.93 | 2.08 | 1.9 | 1.07 | 1.04 | 1.36 | 1.63 | 1.68 | 1.51 | 1.15 | 0.58 | 0.4
 | 0.49137 | 0.34609 | 0.20082 | 0.15809 | 0.11964 | 0.22646 | 0.49137 | 0.67509 | 0.82891 | 1.1921 | 1.4271 | 1.6578 | 1.7775 | 1.6792 | 1.3545 | 0.87164 | 0.96564 | 1.3502 | 1.5724 | 1.9185 | 1.6365 | 1.316 | 1.0383 | 0.705
 | 0.5 | 0.31 | 0.18 | 0.14 | 0.16 | 0.2 | 0.38 | 0.73 | 0.9 | 1.01 | 1.29 | 1.51 | 1.64 | 1.85 | 1.9 | 1.02 | 0.89 | 1.22 | 1.43 | 1.72 | 1.59 | 1.34 | 1.18 | 0.93
 | 0.63 | 0.34 | 0.21 | 0.21 | 0.25 | 0.29 | 0.34 | 0.55 | 0.7 | 0.95 | 1.47 | 1.76 | 1.83 | 2.09 | 1.67 | 0.9 | 0.97 | 1.14 | 1.45 | 1.86 | 1.76 | 1.11 | 0.85 | 0.69
 | 0.59 | 0.3 | 0.22 | 0.12 | 0.17 | 0.36 | 0.47 | 0.61 | 0.87 | 1.14 | 1.18 | 1.47 | 1.56 | 2.2 | 1.66 | 1 | 1.08 | 1.48 | 1.32 | 1.68 | 1.68 | 1.42 | 0.78 | 0.64
Spent almost a year recopilating and geoprocessing the information for the whole country

## Slide 11: Transport – On-road traffic (SNAP07)
Methodologies for the emission estimation
EMEP/EEA - COPERT IV  Exhaust (hot&cold), evaporative and tyre/break/road wear emissions
Pay et al, 2010  Paved road dust resuspension emissions
Composition fleet based on real circulation data per district
12 fleet composition profiles obtained from Remote Sensign Device (RSD) data
AB, 2010
According to city council of Barcelona (2010), NOx emissions estimated in Barcelona using the RSD data are 16.2% higher than the ones obtained using CORINAIR EF.
EMEP/EEA does not include a methodology for estimating paved road dust resuspension emissions

## Slide 12: Transport – On-road traffic (SNAP07)
Other cities without traffic information
EFs [t/year/inhabitants] obtained from cities with available information
EF other cities [kg/hab/year] |  |  |  |  |  |  |  | 
 | NOx | NMVOC | SOx | CO | NH3 | TSP | PM10 | PM2,5
HERMES v 2.0 | 3,01 | 0,66 | 0,04 | 3,96 | 0,04 | 0,48 | 0,44 | 0,34
Applied to 745 municipalities
The emissions estimated represent a 28% and 23% of the total NOx and TSP on-road traffic emissions
Specific methodology for estimating urban emissions in cities without traffic information

## Slide 13: Transport – Other mobile sources (SNAP08)
Port  Emissions per type of operation (maneuvering/hotelling) obtained using the Entec UK methodology
Annual SOx emissions (1km*1km)
Airport  LTO cycles emissions obtained using EMEP/EEA guidebook
Hourly NOx emissions
Land-based port related emissions (e.g. vehicle traffic, loading/unloading operations) are significant, but they are not included in the EMEP/EEA guidebooks.

## Slide 14: Rating of the database used
Data Attribute Rating System (DARS) (USEPA, 2003)
Activity - SNAP sectors | Score | Information sources
SNAP0101 - Public power stations | 76,0 | Emission factors: Measurements from the Spanish National Office of Emission Control for Large Combustion Facilities (OCEM-CIEMAT), TNO (1995), EEA (2007), EEA (2009) Activity data: UNESA (2009), REE (2009a), IEAs(*) and ERs(**) Temporal profiles: REE (2009b)
SNAP0103 - Petroleum refining plants | 47,3 | Emission factors: EEA (2009), EEA (2007) Activity data: Oilgas (2009), IEA and ER by facility, , MINECO (2003)
SNAP010406 - Coke oven furnaces | 61,3 | Emission factors: EEA (2009), EEA (2007) Activity data: MINETUR (2009a), IEAs(*) and ERs(**), E-PRTR (2009)
SNAP02 - Non industrial combustion plants | 49,0 | Emission factors: EEA (2009) Activity data: MINETUR (2009b), CORES (2010), IDAE (2010B) Temporal profiles: USEPA (2002); CORES (2010); ENAGAS (2010)
SNAP030103, SNAP030104 & SNAP030105 - Cogeneration plants | 61,5 | Emission factors: EEA (2009), EEA (2007) Activity data: MINETUR (2009c), REE (2009), IEA and ER by facility, E-PRTR (2009) Temporal profiles: REE (2009)
SNAP030203, SNAP030302 & SNAP040202 to SNAP040207 - Iron and steel industry | 50,3 | Emission factors: EEA (2009), EEA (2007), TNO (1995) Activity data: E-PRTR (2009), UNESID (2009), IEAs(*) and ERs(**) Temporal profiles: Assumed constant activity profile
SNAP030305, SNAP030306, SNAP030322 & SNAP040301 - Non-ferrous metal industry | 54,3 | Emission factors: EEA (2009), EEA(2007) Activity data: IEAs(*) and ERs(**) Temporal profiles: Assumed constant activity profile
SNAP030311 & SNAP040612 - Cement industry | 61,8 | Emission factors: IEA and ER by facility, Measurements from the Catalonia's Atmospheric Emission Network (XEAC), MMA (2004), EEA (2009), Activity data: IEAs(*) and ERs(**), OFICEMEN (2009), E-PRTR (2009)
SNAP030312 & SNAP040614 - Lime industry | 50,3 | Emission factors: EEA (2009), EEA (2007), TNO (1995) Activity data: IEAs(*) and ERs(**), MAGRAMA (2007a), ANCADE (2009), E-PRTR (2009)
SNAP030314 up to SNAP030318 - Glass industry | 50,3 | Emission factors: EEA (2009), EEA (2007) Activity data: ANFEVI (2009), IEAs(*) and ERs(**), MAGRAMA (2007a), E-PRTR (2009), ARDAN (2009) Temporal profiles: Assumed constant activity profile
SNAP030319 - Bricks and tiles industry | 50,3 | Emission factors: EEA (2009), EEA (2007) Activity data: HYSPALIT (2009), IEAs(*) and ERs(**), MAGRAMA (2007a), E-PRTR (2009)
SNAP030320 - Fine ceramic materials industry | 50,3 | Emission factors: EEA (2009), EEA (2007) Activity data: ASCER (2009), IEAs(*) and ERs(**), MAGRAMA (2007a), E-PRTR (2009), ARDAN (2009)
SNAP040101, SNAP040102 & SNAP040103 - Processes in petroleum industries | 57,0 | Emission factors: EEA (2009), EEA (2007) Activity data: Oilgas (2009), IEAs(*) and ERs(**), E-PRTR (2009) Temporal Profiles: MINETUR (2009d)
SNAP040401 - Sulfuric acid industry | 54,0 | Emission factors: EEA (2007) Activity data: IEAs(*) and ERs(**), E-PRTR (2009)
SNAP040602 & SNAP040603 - Paper pulp industry | 50,3 | Emission factors: EEA (2009), EEA (2007) Activity data: ASPAPEL (2009), IEAs(*) and ERs(**), MAGRAMA (2007a), E-PRTR (2009), ARDAN (2009)
SNAP07 - On-road transport | 76,5 | Emission factors: EEA (2009), Pay et al. (2010) Activity data & Temporal profiles: MF (2009), Observation stations managed by Spanish Governmental Authorities (Central Government, Autonomous Communities, Provinces and City Councils), Tele Atlas ® Multinet ® (2011), DGT (2010), AB (2010), AM (2009)
SNAP0804 - Maritime activities | 65,8 | Emission factors: Cooper & Gustafsoon (2004) Activity data: Spanish port authority’s annual reports (AAPP), SPS (2009), Entec UK Limited (2007, 2010), Corbett et al. (2003) Temporal profiles: SPS (2009), Localizatodo.com
SNAP0805 - Air traffic (LTO cycles < 1000m) | 71,3 | Emission factors: EEA (2009), USEPA (2005), ICAO (2010), FOCA (2007) Activity data & Temporal Profiles: AENA (2009)
SNAP0806 - Agricultural machinery | 51,8 | Emission factors: EEA (2009) Activity data: MAGRAMA (2007b and 2009b) Winther and Nielsen (2006) Temporal Profiles: EEA (2009)
SNAP09 - Waste treatment | 76,0 | Emission factors: Emissions measured from Catalan Atmospheric Emission Network (XEAC) and AEVERSU (2009), EEA (2009) Activity data: AEVERSU (2009), Oilgas (2009), IEAs(*) and ERs(**) Temporal profiles: XEAC, MINETUR (2009e)
(*) Integrated Environmental Authorizations by facility; (**)Environmental Reports by facility |  | 

## Slide 15: Speciation process – HERMESv2.0 to CMAQ
NMVOC & NO2  Speciation profiles obtained from the EMEP/EEA guidebook
SPECIATE 4.2
CBIV / CB05 / MELCHIOR2
CMAQ 5.0.1
Hao et al., 2012
NMVOC & PM2.5  Used > 50 profiles (SPECIATE 4.2)
NO2  Applied a constant NO/NOx ratio of 0.9
On-Road Traffic
Other sectors
Lack of an European speciation database
Lack of information for NO/NOx ratios

## Slide 16: What we expect from fairmode

## Slide 17: Energy-Industry-Waste (SNAP01-03-04-09)
Activity data
  Energy sector  Energy forecasting demand
  Industry  Not all the E-PRTR facilities report complete information
Emission data
  In some cases, EF reported by EMEP/EEA guidebook are too general (not discriminated by fuel used), specially in the industrial sector (SNAP03-04)
Spatial allocation
  No comments
Temporal allocation
  No comments
Chemical speciation
  Development of a complete European speciation database

## Slide 18: Residential-Commercial (SNAP02)
Activity data
  Development of a database with local information on biomass consumption
Emission data
  No comments
Spatial allocation
  Development of a spatial proxy with high resolution for the allocation of biomass combustion emissions
Temporal allocation
Chemical speciation
  Development of a complete European speciation database

## Slide 19: Transport – On-road traffic (SNAP07)
Activity data
  Development of a complete geographically referenced database with traffic flow information from all the European countries. Easy to use with GIS software
Emission data
  Revision of the EF reported by EMEP/EEA guidebook (based on COPERT IV)
  Development of a methodology for estimating road dust resuspension emissions
Spatial allocation
  No comments
Temporal allocation
  No comments
Chemical speciation
  Update the speciation profiles reported by EMEP/EEA, increasing the number of categories.

## Slide 20: Transport – Other mobile sources (SNAP08)
Activity data
  No comments
Emission data
  Development of a methodology for estimating Land-based port related emissions (e.g. vehicle traffic, loading/unloading operations)
Spatial allocation
  No comments
Temporal allocation
  No comments
Chemical speciation
  Development of a complete European speciation database

## Slide 21: Thank you!