## Slide 1: Applying the DELTA-FAIRMODE tool to support AQD: the validation of the TCAM Chemical Transport Model
C. Carnevale, G. Finzi, A. Pederzoli,
P. Thunis, E. Pisoni, M. Volta

## Slide 2: Outline
Methodology
TCAM model
Results
Conclusions

## Slide 3: MPC definition
MODEL PERFORMANCE CRITERIA (MPC):
“minimum level of quality to be achieved by a model for policy use” (Boylan and Russell, 2006)

## Slide 4: Model evaluation: Main Statistical Indicators

## Slide 5: Model Performance Criteria

## Slide 6: Target Diagram
RMSEU≤0.5  RMSE < U  model results are on average within the range of the observation uncertainty for that station any attempt to improve the model performance further is unhelpful.
0.5<RMSEU≤1  RMSE on average > the range of U but the model might still be closer to the “true value” (i.e. the perfect measurement) than observations.
RMSEU>1 observations are closer to the “true value” than the model results.

## Slide 7
Measures: 50 monitoring sites (suburban, urban and rural background)
Model: TCAM
Year:2005
Domain resolution:6x6km2 (POMI exercise)
Pollutants: O3 – PM10

## Slide 8: TCAM: Transport and Depostion Module
Eulerian 3D model
Terrain-following coordinate system
Horizontal Transport Module: Chapeau Function + Forester Filter
Vertical Transport Module: Crank-Nicholson hybrid solver based on the vertical diffusivity coefficient
Deposition Module
  Dry deposition: resistance-based approach
  Wet deposition: scavenging approach for both gas and aerosol species

## Slide 9: TCAM: Gas chemical module
Chemical Mechanism
  CBIV 90
  SAPRC 90/97
  COCOH 97
Numerical Solver
  QSSA (explicit)
  IEH (hybrid)
Species: 95
Reactions: 187
Fast-Species (12): LSODE (implicit)
Slow-Species: Adams-Bashforth (explicit)

## Slide 10: TCAM: Aerosol module
Chemical Species: 21
  12 inorganics
  9 organics
Size Classes: <10 (from 0.01 mm to 50 mm)
  Fixed moving approach
Involved Phenomena:
  Condensation/Evaporation
  Nucleation
  SO2 aqueus chemistry
Shell
Core

## Slide 11: Where using Delta?
Land use
Topography
Prognostic
output
PROMETEO
TCAM
Continental scale model output
BOUNDY
Boundary and
Initial condition
3D concentration
fields
POEM-PM
Emission inventories
Emission Fields
3D wind and temperature fields Turbolence and Boundary Layer parameters
VOC speciation
Profiles
Temporal
Profiles
Output
PM size and chemical speciation
Profiles
GAMES: Gas Aerosol Modelling Evaluation System
Notes: Mi fa schifo questo titolo… Vogio introdurre le due slide successive su delta e meteo…
system is composed by (i) a meteorological preprocessor,
simulating the wind and temperature
fields and the turbulence parameters over the domain,
(ii) an emission processor, estimating emission
fields for the emitted species alternative emission
scenarios, (iii) a photochemical model that
describes the transport and the chemical transformations
taking place in the atmosphere.

## Slide 12: Target diagram: PM10 daily mean
Systematic error: Bias <0 (underestimation)
Random error: problem with correlation!
69% of sites respect the MPCRMSE

## Slide 13: Issue: What data to be used? (1/3)
Selecting a subset of station?
  Limited number of stations
  Different regimes
Selecting a subset of data for each stations?
  Considering only the X% of the best data (X-th percentiles)

## Slide 14: Issue: What data to be used? (2/3)
90% Stations
90% Data

## Slide 15: Issue: What data to be used? (3/3)
Default Setup
90% Data
85% Data
80% Data

## Slide 16: Issue: How good is “good”?
90% of station
inside the
“acceptance region”
Good
Very Good
Excellent
Notes: Controllare inglese nel titolo!

## Slide 17: Target Plot: O3 8hmax
Worse than PM10?
Similar to other POMI model
O3
NO2, PM10
k=1.44
k=2

## Slide 18: Issue: coverage factor k value?
k=1.44
k=1.75
k=2.00
Similar to PM10

## Slide 19: MQO extension to meteorology: WS
WS
Uncertainty constant (0.5 m/s) below 5m/s (WMO)
Uncertainty proportional to WS (10%) above 5m/s (WMO)
Rounding (to integer) effects accounted for
Chart: m/s
Parameter | Value
Alpha | 0.88
URV | 0.14
RV | 5
EC4MACS 2009 (450 st) |  | 
R | 0.78 | 
Bias | 36% | 1.3 m/s
NMSD | 63% | 

## Slide 20: MQO extension to meteorology: TEMP
TEMP
Instrument uncertainty on test-bank  0.1K
Instrument uncertainty in the field  0.5-0.6K
Uncertainty including meteo-housing structure  1K
Parameter | Value
Alpha | 1.0
URV | 0.04
RV | 25
EC4MACS 2009 (460 st) | 
R | 0.96
Bias | 2K
NMSD | 26%

## Slide 21: Conclusions & Discussions
About Delta tool
  Very valuable tool for the model (of different type…) validation/comparison
  Continuosly improving/generalizing (Thanks!!!)
About MPC
  Issue1: Considering all the data?
  Issue2: What value of U?
About TCAM
  Quite interesting and good performances
    PM10: Very good
    O3: comparable to other model
  Are the performances good enough?
Chart: 
% Station inside "acceptance region" | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
?

## Slide 22: Thank you