## Slide 1: UK feedback on Delta V3.0
Presented by: John Stedman, Daniel Brookes, Keith Vincent, Emily Connolly
10 April 2013

## Slide 2: Outline
Practical aspects
Other aspects covered in accompanying presentation
  Use of models for UK compliance assessments
  Feedback provided last year
  Using Delta V3.0
  Conclusions and recommendations
Views of the UK Competent Authorities

## Slide 3: Models for UK compliance assessments
  Pollution Climate Mapping (PCM) models as supplementary assessment methods for annual compliance assessment (Decision 2004/461/EC)
  SO2, NOx, NO2, PM10, Pb, C6H6, O3, PM2.5, As, Cd, Ni and B[a]P
  Annual mean
  Pollutant specific metrics
    High percentiles for SO2 and AOT40 and days above threshold for O3

## Slide 4: Models for UK compliance assessments
  Pragmatic dispersion model
    Large point sources – modelled using the air dispersion model ADMS and emissions estimates from the UK National Atmospheric Emissions Inventory (NAEI)
    Small point sources – modelled using the small points model and NAEI emissions
    Distant sources – characterised by the rural background concentration. From measurements or results from other models
    Area sources – modelled using a dispersion kernel and emissions estimates from the NAEI.
    Roadside increment model for traffic locations

## Slide 5: Models for UK compliance assessments
  Assessment is based on a combination of measurement data and model results. The compliance status for each zone is based on the maximum of the measured and modelled concentrations

## Slide 6: Models for UK compliance assessments
  The models are designed to assess compliance at locations defined within the directives
    Urban (and Rural) Background locations: 1 km x 1 km grid squares representative of the exposure of the general population
    Traffic locations: ~9000 receptors 4 m from the kerb of major roads in urban areas (to be representative of more than 100m segment and more than 25m from junctions.
  The same models are used for
    Extent of exceedance
    Source apportionment
    Projections for the development of air quality plans
    Consistent with the assessment for the reference year

## Slide 7: Feedback from 2012
Easier input of annual mean data 
75% data capture threshold 

## Slide 8: Delta V3.0: PCM model results for NO2 in 2010
  Problems with file headers now resolved
    Manual had
    an additional “;”

## Slide 9: Delta V3.0: PCM model results for NO2 in 2010
  In previous version had to enter 8760 identical values
    If you do this in V3.0 DQO for hourly are used in the plot

## Slide 10: Delta V3.0: PCM model results for NO2 in 2010
  Parameter values in V3.0 (left) are not consistent with the paper circulated on 5 March 2013 (right)

## Slide 11: Delta V3.0: NO2 in 2010 and 2011
  Model performance varies from year to year
    Using parameters from 5 March 2013 paper

## Slide 12: Delta V3.0: NO2 2011
  With (left) and without 2 term (right)
    Using parameters from 5 March 2013 paper

## Slide 13: Delta V3.0: PCM PM10 in 2010
  Reproduced in spreadsheet calculations

## Slide 14: Delta V3.0: PCM PM10 in 2010
  Using parameter values from 5 March paper (left)
  Using parameters for TEOM (FDMS) (right)

## Slide 15: Conclusions and recommendations
Input of annual data much easier
Parameters in Delta V3.0 do are not consistent with the circulated paper
  Assessment of model performance is highly sensitive to the selection of parameters
Recommendations
  Include parameter values in Delta plots for version control
  Allow users to choose non-default values to explore sensitivities
  Will need to address all the AQD and DD4 pollutants