## Slide 1: Swedish experiences of applying the Quality Objectives for NO2 and PM10 modelling
introduction
model evaluation for Swedish - street/road stations - urban background stations
discussion and conclusions
by L. Gidhagen, G. Omstedt and S. Andersson

## Slide 2: Model quality objectives (uncertainty) as described in the AQ directive
Modelling uncertainty | NO2 PM10
Hourly | 50 % -
Daily average | 50 % -
Annual average | 30 % 50%
The uncertainty of modelling estimation is defined as the maximum deviation between the measured and calculated concentration levels for 90 % of individual monitoring points, without taking into account the timing of the events. The average annual modelling uncertainty
for NO2 is defined as ±30% and for percentiles ±50%
Fairmode http://fairmode.ew.eea.europa.eu/
Op and Mp are the observed and modelled concentrations at the percentile (p)
OLV and MLV are the closed observed and measured concentration to the limit value
concentration (LV)
Indicators for model quality
Notes: MRPE= Maximum Relative Percentile Error
MRDE= Maximum Relative Directive Error

## Slide 3
Gidhagen, L., Johansson, H. and Omstedt, G., 2009: SIMAIR - Evaluation tool for meeting the EU directive on air pollution limits. Atmospheric Environment, 43, 1029-1036, doi:10.1016/j.atmosenv.2008.01.056.
Andersson, S. och Omstedt, G., 2009: Validering av SIMAIR mot mätningar av PM10, NO2 och bensen. Utvärdering för svenska tätorter och trafikmiljöer avseende år 2004 och 2005. SMHI Meteorologi, Nr. 137, 125 pp. (In Swedish).
SIMAIR
Model validation in Sweden
~ 30 road/street stations
~ 20 urban background stations

## Slide 4: Validation performed using both RPE and RDE
Swedish EPA recommends the use of RPE for quality check of hourly (NO2) and daily (PM10, NO2) values.
Swedish EPA supports FAIRMODE recommendation to use, for annual mean values, the RDE calculation when observed value is low compared to limit value. For high observed annual mean values, RPE can be used.
We are left with some confusion, e.g.: - Not clear when to use RDE or RPE - Not clear how the 90% of the station comparisons are selected: - How big can the area be (entire Sweden)? - Should the comparison include only one specific year or can we include comparisons for the same station but for two different years? - Why is max(RPE) or max(RDE) selected, would not median be more useful? Or both?
Validation results from 2004 and 2005

## Slide 5
Model simulations of PM10 for street level show acceptable quality, even for 98-percentiles
Differences MRPE and MRDE?
Validation PM10 from 2004 and 2005

## Slide 6
Validation PM10 from 2004 and 2005 using RPE and RDE
With RDE the quality is OK, with RPE it is almost OK (although MRPE for daily PM10 is still not defined)

## Slide 7: RPE and RDE for PM10
There are often a few “poor” stations where measurement errors or bad siting (low representativeness) can be suspected
Could med(RPE) and med(RDE) be a better alternative?
Same station

## Slide 8
Examples for PM10: How will RPE differ from RDE?
Annual mean: RPE = 1% RDE = 6%
Annual mean: RPE = 30% RDE = 18%
Annual mean: RPE = 44% RDE = 20%
Hornsgatan/Stockholm year 2000
Kungsgatan/Norrköping year 2004
Eriksgatan/Landskrona year 2004
Graphs illustrate RPE and RDE for daily 90-percentiles

## Slide 9
Modell evaluation of NO2 at street/road level
Model simulations of NO2 for street level show acceptable quality, even for hourly values

## Slide 10
Validation NO2 from 2004 and 2005 using RPE and RDE
Daily and hourly percentiles OK, annual means almost OK

## Slide 11
Improvements in the model can be demonstrated by improved RPE
The current quality objectives are still not fully compliant in urban background annual mean values
BUM new:
MRPE annual mean = 0.40
MRPE 98-percentile daily mean = 0.48
MRPE 90-percentile hourly mean = 0.49
Modell evaluation of NO2 in urban background using RPE

## Slide 12
Example: SIMAIR for PM10
PM10 | annual mean | 90-percentil
MRPE | 0.39 | 0.51
MRDE | 0.24 | 0.45
Can we use MRPE and MRDE as uncertainties on the simulated levels?
Example: calculated yearly mean PM10 concentration is 25 µg/m3 and
calculated 90-percentil is 45 µg/m3 then the uncertainties are: MRPE:
Yearly mean: 25 +/- 9.8 µg/m3 i.e. between 15.3 - 34.8 µg/m3
90-percentile (daily mean): 45 +/- 23.0 µg/m3 i.e. between 22.1 - 68.0 µg/m3
MRDE:
Yearly mean: 25 +/- 9.6 µg/m3 i.e. between 15.4 - 34.6 µg/m3
90-percentile (daily mean): 45 +/- 22.5 µg/m3 i.e. between 22.5 - 67.5 µg/m3
Likely those intervals are too large for a general public?
Can MRPE and MRDE be used as uncertainties?

## Slide 13
Are the quality objectives (QA) obtainable and relevant?
Answer: Yes, but…
Some confusion on how to calculate MRPE and MRDE which must be eliminated.
The indicator should reflect model uncertainty as much as possible. In our opinion RPE is a better indicator than RDE, especially for Swedish conditions with air quality levels often well below the limited values.
It is unclear if and how these indicators can be used, except for showing compliance of Directive’s “Quality objectives for models”. For describing model uncertainties in a broader sense other and more refined indicators are needed (Delta tool…).
Conclusions
Thank you for your attention!

## Slide 14
PM10 in Swedish cities (2004): Importance of local contribution

## Slide 15
PM10 in Swedish cities (2004): Local – Urban - Regional

## Slide 16
PM2.5 in Swedish cities: Local – Urban - Regional